## Slide 1
Evaluation of the Maximal Modulation Frequency for Wow and Flutter Determination
Acknowledgements
Research funded by the Commission of the European Communities, Directorate-General of the Information Society within the Integrated Project No. FP6-507336 entitled: “PRESTOSPACE – Preservation towards storage and access. Standardized Practices for Audiovisual Contents Archiving in Europe”.
Przemyslaw Maziewski e-mail: p_maziewski@pg.gda.pl
Gdansk University of Technology, Multimedia Systems Department Narutowicza 11/12, 80-952 Gdansk, Poland
Wow Determination Algorithms
Introduction
An audio material can be contaminated by several distortions leading to sound quality deterioration. Among many distortions present in analogue audio recordings wow and flutter (referred further as wow) are common and difficult to compensate. Wow could be found in old gramophone recordings, wax cylinders, audio cassettes and also on the magnetic and optical sound tapes.
The main source of the distortion is the irregular velocity of the sound carrier. Motives for this can be found in:
- audio path components excentricity or ellipticity,
- motor speed fluctuations,
- carrier damages (loss of perforation),
- inappropriate production techniques (tape cuts & joins).
Engineers from the Gdansk University of Technology developed several methods for the distortion reduction, however, there was no study of their maximal determined modulation frequency. This poster presents such a study for three algorithms: the power-line hum tracker, high frequency bias tracker, and centre of gravity tracker
ISSVEM
2007
Power-line hum tracker
Power-line hum is commonly found in archival recordings. Based on the assumption that its frequency was stable during the recording, it is possible to estimate wow characteristic through observation of hum frequency deviations. Since the frequency of hum is very low (50-60Hz) it is hard to analyse it with sufficient precision using traditional, DFT-based methods. Therefore a solution based on autoregressive modelling was implemented.
For each algorithm three test signals were prepared. Each signal – a pure sinusoidal tone with a constant carrier frequency – was modulated with a simple FM pattern equalling a half, whole, and a double FMmax. The carrier frequencies were set to: a) 50 Hz for the hum tracker, b) 3150 Hz for the COG tracer, c) 30 kHz for the bias tracker. Next the modulated signals were processed by the tracing algorithms and the resulting PVCs were compared against the known FM patterns
Maximal modulation frequency
In order to establish the maximal modulation frequency (FMmax) two factors must be analyzed:
a) the Nyquist sampling theorem for the discrete wow characteristic (PVC):
where M represents the frame length and Fs the sampling frequency
b) the quasi-stationarity criteria for the infra-frame modulations:
Knowing the typical Fs values of the distorted signals and the typical frame lengths of the presented algorithms, the FMmax can be calculated:
The FMmax is determined mostly by the quasi-stationarity criteria. Based on the criteria it can be stated that all of the algorithms can track wow modulations. The hum tracker can determined flutter modulations up to 12 Hz approximately; the COG tracker can determine flutter up to 20 Hz approximately; and the bias tracker can determine full range of flutter modulations
The high frequency bias signal (HFB) is added to the tape recorder's head during the recording process. Since the bias frequency is initially constant, therefore wow may be reflected by deviations of the HFB signal and easily used to retrieve the distortion characteristic.
Time [s]
Frequency [kHz]
High frequency bias track
The detection process of the bias signal frequency is based on the smoothed spectrogram. Smoothing of the spectrogram image is performed in time and frequency domain. An appropriate high-pass filtering is performed to prevent influence of low frequency components on the signal during the HFB detection. Additionally, each spectrum (each column of the spectrogram matrix) is weighted by the preemphasis curve.
High-frequency bias tracker
Centre of gravity tracker
Tonal track
Time [s]
Frequency [kHz]
Power-line hum track
Time [s]
Frequency [kHz]
The approach involves an operator who selects the time-frequency region with the varying tonal component. Based on the selection, the spectral centre-of-gravity is calculated in successive time frames, and is used to compute the final wow characteristic
Experiments and conclusions
Simulation results of the COG tracking
Simulation results of a artificial hum tracking
Simulation results of an artificial bias tracking