## Slide 1
Accidental Wow Evaluation Based on Sinusoidal Modeling and Neural Prediction
Acknowledgements
Research funded by the Commission of the European Communities, Directorate-General of the Information Society within the Integrated Project No. FP6-507336 entitled: “PRESTOSPACE – Preservation towards storage and access. Standardized Practices for Audiovisual Contents Archiving in Europe”.
Przemyslaw Maziewski, Lukasz Litwic and Andrzej Czyzewski e-mail: {przemas, llitwic, andcz}@sound.eti.pg.gda.pl
Gdansk University of Technology, Multimedia Systems Department Narutowicza 11/12, 80-952 Gdansk, Poland
Experiments and conclusions
Experiment 1 - Wow characteristic evaluation
Experiment 2 – Linear Prediction (LP) vs. Neural Nets (NN)
Experiment 3 - Prediction Enhanced by Nureal Net
The Algorithm for Wow Evaluation
Introduction
Wow defect is a distortion defined as parasitic frequency modulation and it
is perceived as pitch fluctuation of audio program. It is introduced into audio
by tape speed fluctuations, its damages or inappropriate editing techniques.
The perceived pitch variation comes from the fact that wow modulates the spectral components of audio signal. The estimation of parasitic modulation waveform (PVC) can be performed by the analysis of spectral components variations.
The first part presents the algorithm for wow determination based on sinusoidal modelling. The algorithm is dedicated to accidental wow defect determination, which is characterized by a short duration and a strong modulation. The short duration of the defect allows analyzing it independently of genuine pitch variations of audio signal.
The second part concerns the employment of a neural-network-based prediction for enhancing the partial tracking process. The neural network (NN) prediction is also compared to linear prediction (LP).