## Slide 1
Time-Domain, autocorrelation pitch variation curve detector
Introduction
An audio material can be contaminated by several distortions leading to sound quality deterioration. Among many defects present in analogue audio recordings wow is common and difficult to compensate. It could be found in old gramophone recordings, wax cylinders, audio cassettes and also on the magnetic and optical sound tapes.
The main source of the defect is the irregular velocity of the sound carrier. Motives for this can be found in:
- audio path components excentricity or ellipticity,
- motor speed fluctuations,
- carrier damages (loss of perforation),
- inappropriate production techniques
(tape cuts & joins).
Engineers from the Gdansk University of Technology developed several methods for the defect reduction. We also introduced an application combining results generated by the algorithms. The application provides additional options for sound visualization and useful tools for manual refitting of the wow characteristics.
New Algorithms for Wow and Flutter Detection and Compensation in Audio Paper 6353
Acknowledgements
Research funded by the Commission of the European Communities, Directorate-General of the Information Society within the Integrated Project No. FP6-507336 entitled: “PRESTOSPACE – Preservation towards storage and access. Standardized Practices for Audiovisual Contents Archiving in Europe”.
Andrzej Czyzewski , Marek Dziubinski, Andrzej Ciarkowski, Maciej Kulesza,
Przemyslaw Maziewski, and Jozef Kotus e-mail: ac@pg.gda.pl
Gdansk University of Technology, Multimedia Systems Department Narutowicza 11/12, 80-952 Gdansk, Poland
Experiments and conclusions
The presented autocorrelation based method’s result as well as listening tests show that the engineered algorithm is robust enough to deal with noisy and complex real-life audio signals.
Algorithm for high-frequency bias tracking in magnetic recordings
Algorithm for tracking power-line hum frequency
PVC
BIAS
PVC
PVC
Wow Evaluation
Algorithm 1
“DeWower”
C++ application
VST 2.0
Samples buffers
Wow Reduction
Algorithm 1
Samples buffers
„DeWower” Application
The application provides :
- methods for algorithms testing,
- GUI optimised for the proposed algorithms,
- semi-manual methods for wow evaluation;
Spectrograms
Time (s)
Frequency (Hz)
Lags
Amplitude
Autocorr. sequences
Harmonic signal of constant pitch is periodic, while signal with similar harmonic properties, but time varying pitch can be viewed as aperiodic which is indicated by their autocorrelation sequences.
A
B
A
B
A
B
Periodicity indicator
Max periodicity for slope = 1
Max periodicity for slope = 1.5
Periodicity indicator vs PVC slopes
Periodicity indicator value
Spectrogram vs local slopes
Spectrogram vs constructed PVC
Input is divided into short segments and non uniformly resampled for various PVC slopes in order to find the largest periodicity indicator value
Global PVC is constructed of local PVC slopes
SPECTROGRAM AND PVC OF THE INPUT SIGNAL
SPECTROGRAM OF THE OUTPUT SIGNAL
The high frequency bias signal (HFB) is added to the tape recorder's head during the recording process. Since the bias frequency is initially constant, therefore wow disturbance may be reflected by deviations of the HFB signal and easily used to retrieve the disturbance’s time domain properties.
Time [s]
Frequency [kHz]
High frequency bias track
The detection process of the bias signal frequency is based on the smoothed spectrogram. Smoothing of the spectrogram image is performed in time and frequency domain. An appropriate high-pass filtering is performed to prevent influence of low frequency components on the signal during the HFB detection. Additionally, each spectrum (each column of the spectrogram matrix) is weighted by the preemphasis curve.
The detection of HFB frequency fluctuations allows for nearly perfect estimation of the PVC. It can be noted from the spectrogram image of the restored sound sample that the frequency of the bias signal remains constant over time.
Power-line hum is commonly found in archival recordings. Based on the assumption that its frequency was stable during the recording process, it is possible to estimate PVC flow through observation of local hum frequency deviations. Since the frequency of hum is very low (50-60Hz) it is hard to analyse it with sufficient precision using traditional, DFT-based methods. Therefore a solution based on autoregressive modelling was implemented.
Spectrogram of hum and PVC estimate based on it
Spectrogram of hum and PVC estimate based on it
Algorithm for tracking power-line hum frequency allows for precise estimation of PVC flow with certain class of input signals. In the example below previously presented signal has been restored and the frequency of hum remains stable.