## Slide 1: Wow Restoration in Movie Soundtracks A. Czyzewski, P. Maziewski, M. Dziubinski, A. Ciarkowski, M. Kulesza, J. Kotus & B. Kostek ac@pg.gda.pl
Prepared wow restoration plug-in
Defect origin
The wow is a common and a difficult to compensate type of audio distortion. It could be found in separate magnetic tapes as well as on the optical tapes where the audio is placed next to the perforation.
The main source of the defect is the irregular velocity of the sound carrier. Causes of wow can be found in:
- audio path components excentricity or ellipticity,
- motor speed fluctuations,
- carrier damages (loss of perforation),
- inappropriate production techniques (tape cuts & joins).
PRESTOSPACE project participants from the Gdansk University of Technology (PL) developed several methods for the wow defect restoration.
Spectral Content Analysis
To obtain wow characteristics the audio spectrogram can be analysed. The proposed algorithms tracks chosen spectral sinusoidal components whereby the wow variations are evaluated.
Detected components form trajectories depicting the defect with high accuracy. Based on further statistical post-processing the general wow characteristic is found.
Scanning for trajectories can be performed in several spectral-based domains:
- DFT based sinusoidal sound analysis,
- Smoothed spectrum representation,
- DFT based spectrum centre of gravity;
Time-Domain Based Method
The input signal is divided into short segments, and each of such segments is then analyzed in order to determine PVC (Pitch Variation Curve). The PVC changes are tracked in the following way:
- Current segment is non-uniformly resampled with
various PVC slopes.
Autocorrelation sequences are calculated for each re-
sampled version of a current block.
The most regularly periodic resampled version is treated as locally constant (in terms of PVC variations).
Periodicity is indicated by the Autocorrelation sequence
envelope properties.
After calculating local PVCs, the global PVC is recursively
built from the fragments estimating local slopes.
Carrier Feature Analysis
Power-line hum is commonly found in archival recordings. Based on the assumption that it was introduced into audio path during the recording phase and was subject to the same wow distortion as the useful signal, it is possible to estimate the depth of a wow effect through the tracking of the hum frequency.
Due to relatively low frequency of hum it is practically impossible to analyze it with satisfactory time/frequency resolution employing traditional DFT methods. Therefore a method based on autoregressive model was proposed. The method has been evaluated employing some real-life examples and proved to be effective both in terms of analysis quality and computational cost.
High frequency bias (HFB) signal which is introduced to the magnetic tape during the recording process serves as an ideal target for parasite wow characteristic determining.
Since the bias signal is of high frequency, the STFT analysis provides a suitable tool to deal with the problem of detecting time-frequency variations. The smoothing of the spectrogram, both in time- and in frequency-domain as well as preemphasis applying allow reducing the influence of the HFB amplitude irregularities on the PVC detection.
Assuming that HFB is present on the tape, the engineered algorithm works very robustly in terms of PVC detection and allows an effective signal restoration.
R E S T O R E
Wow
No Wow