## Slide 1: Movie Soundtrack Wow Restoration A. Czyzewski, P. Maziewski, M. Dziubinski, A. Ciarkowski, M. Kulesza, J. Kotus & B. Kostek ac@pg.gda.pl
Defect origin
Wow is a common and a difficult to compensate type of audio distortion. It could be found in magnetic and optical sound tapes. The main source of the defect is the irregular velocity of the sound carrier. Causes of wow can be found in:
- audio path components excentricity or ellipticity as well as in motor speed fluctuations,
- carrier damages (loss of perforation) and inappropriate production techniques (tape cuts & joins).
PRESTOSPACE project participants from the Gdansk University of Technology (PL) developed an application combining several developed algorithms and additional graphical routines for wow compensation
DeWower application – audio analysis
Power-line hum is a defect typical for recordings coming from pre-digital era. Its presence may be effectively exploited in order to estimate the characteristics of wow disturbance. Due to its low frequency this signal is very hard to analyze. Therefore, engineered plugin utilizes methods typically found in seismology applications to overcome shortcomings of classical Fourier analysis.
The high-frequency-bias signal is added to recorder’s head during the recording process. Usually its frequency fluctuations reflect parasite pitch variations of the audio content. Despite low energy and discontinuities of HFB signal, engineered plugin allows analyzing of its properties, and estimating of wow disturbance characteristic. User has an ability to adjust accuracy as well as other parameters of the analysis.
DeWower application – artefacts analysis
It can be noticed that the medium itself can provide sufficient information about the carrier velocity irregularities. Therefore, the first group of the engineered algorithms contains methods dedicated to power-line hum and high frequency bias (HFB) tracking.
Perceptual DeNoiser
VST plugin
Acoustic noise, present in archival recordings is usually non-white
Parasite frequency modulation and wow removal may influence noise stationarity, thus noise reduction is a significant part of the entire wow removal procedure
DeNoiser plugin is a high quality, and user friendly tool, which can be independently used for acoustic noise removal only
In real life recordings parasite artefacts, such as hum or bias, are not always present. Moreover even if available they do not necessary correlate with wow. Therefore there is a need for the wow evaluation algorithms utilizing only genuine audio content analysis. It is worth to notice that this task is more difficult then a ‘simple’ artefacts analysis.
To achieve this several new methods were developed and assessed. Currently available in the DeWower application. utilize audio spectrum analysis. Another algorithms. i.e. innovatory time-based and advance spectral-based routines, are being implemented.
Wow !
No Wow !
R E S T O R E